## Slide 1
Wing Experimentation and Simulation
CLARK-Y and NACA-0010 Aerofoil
Jalendu Africawala
Emmanuelle Fried
Daniel Opoka

## Slide 2: Rib Building Process
Using mold, measure standard stick
Measure out individual parts
Cut
Glue
Remarks
Fast
Sometimes inaccurate—had to recut

## Slide 3: Adding Spars
Threaded spars vertically
Twisted to align horizontally
Top and bottom spars for front and back
Required strength!

## Slide 4: Webbing with balsa
Webbing cutout
Webbing placement
Repeat

## Slide 5: Adding covers at the leading and trailing edge
Leading edge
Trailing edge

## Slide 6: Attaching cap strips to the ribs
Plywood cap strips
Added to the torsional and bending stiffness
Aid in supporting the skin

## Slide 7: Covering the wing with skin
Cutting the nylon to size
Considerable amount of wastage
Fibres aligned parallel to the ribs
Iron
Cut the edges
Overlap top over bottom skin

## Slide 8: Measurements
Bending Stiffness
Torsional Stiffness

## Slide 9: Bending Stiffness and Comparison to individual beams
 | Weight (in N) | Deflection (in cm) | Rib stiffness K (Nm) | Equivalent number of beams, side by side | Equivalent number of beams, stacked vertically
Without Cap-strip | 4.905 | 1.2 | 408.75 | 2.1475 | 1.2902
With Cap-strip | 9.81 | 0.4 | 2452.5 | 12.8847 | 2.3444
For one beam…
For vertical equivalence…

## Slide 10: Torsional Stiffness
Stage of Construction | Moment (in Nm)
1st: Ribs connected by spruce bars | 0.5886
2nd: Balsa webbing | 1.9865
3rd: Plywood on LE and TE | 2.9879
4th: Cap strips on ribs | 3.8308
5th: Skin | 3.9780
Torsional stiffness (in Nm)
1.8736
6.3233
9.5106
12.196
12.664

## Slide 11: Analysis: Comparison to Mathematical Model
Analytical Torsional Stiffness:
G => Material Property
L => Geometrical Property
Stage | Analytical Torsional Stiffness | Experimental Torsional Stiffness | Percent Error between Analytical and Torsional Stiffness
1st | 2.255 | 1.8736 | 16.9%
2nd | 6.912 | 6.3233 | 8.52%
3rd, TE ignored | 13.067 | 9.5106 | 27.21%
4th | ---- | 12.196 | ----
5th | ---- | 12.664 | ----

## Slide 12: RDM6 study of wing rib

## Slide 14
Upper beam:
Rest of the wing rib:

## Slide 15
Results
Displacement on upper beam:
Average percentage error: 0.034%
Largest error: 0.098 mm
Upper beam:
Rest of wing rib:

## Slide 16: Standard NACA 0010 aerodynamic analysis
Neglecting all geometrical parameters
ISA
50,000 and 1,000,000

## Slide 17: AVRO Canada CF-100 Canuck
At sea level
4.24 m, 16 m, 54.9 , and 15000 kg
Velocity trim
Max climb at 42.5 m/s.

## Slide 18: Thank you Questions…?

## Slide 19: Torsional Moment of Inertia